## Slide 1
The Small, Ultra-bright, MCU Controlled, Extra Feature Flashlight!
© 2009 AGTech, property of Albert Gural
This document may not be copied or distributed without consent of the owner.
Albert Gural
AG:XF01-2008/WTMCE

## Slide 2: Table of Contents
Overview of the flashlight/ history
Flashlight parts
Flashlight hardware cross section w/ descriptions
Circuit schematic diagram
Flashlight software flowchart
ASM. Code (AGXF01 OS v1.00)
Specifications about device and IR communication
Suggested IR transmitter hardware, schematic, and asm. code
Specification about charging (and reprogramming) through ports
Data tables/ charts
Operating the flashlight (detailed guide for users)
Pricing/ Package/ Summary

## Slide 3: 1.1 Flashlight/ History
Chapter 1 deals with the history and different flashlight series of the AG flashlights
Section 1.2 deals with the history of the AG flashlights including SF, UF, and XF
Section 1.3 deals with future models including BF’s, AF’s, and μF (not to be confused with microfarad).
Section 1.4 deals with AG:XF01-2008/WTMCE features

## Slide 4: 1.2 History of AG:xF
2004- AG:SF (super flashlight) series, consisted of Perfboard with variety of LED’s, sensors, and a DIP switch.
2005- unnamed series, consisted of 12V “N” battery and white and/or UV and/or IR LED’s, held with glue gun glue.
2006-2007- AG:UF (ultra flashlight) series, flashlight w/ 12V “N” or Li-Ion and tubular body and CREE LED.
2008- AG:XF (X flashlight) series, flashlight w/ MCU and CREE LED in tubular body w/ ID.

## Slide 5: 1.3 Future of AG:xF
AG:BF (bright flashlight) series flashlights plan to incorporate high power Li-Ion cells with High-Brightness Cree LED’s for uses where spotlight brightness is needed.
AG:AF (alkaline flashlight) series flashlights plan to incorporate high brightness Seoul LED’s with a 1.5 to 5v converter to form a high brightness, single AAA cell flashlight.
AG:μF (micro flashlight) series flashlights plan to incorporate the performance of AG:UF series and small size from an 8o lens, CREE XP-E LED, small switches, and 2/5 AAA or 3/5 AAA sized Li-Ion cell.

## Slide 6: 1.4 AG:XF features
Brief of Features:
PIC16F684 microcontroller
Most lights powered by microcontroller
Li-Ion cell
Cree Q5 XR-E LED
IR, RGB, UV, controllable R,G,B LED’s
Constant on backlights for Main switch and power ports
Other backlights
All switches have backlights
8 main modes:
  W: main output mode
  R: Hyperthermia mode
  Y: Flashing Output mode
    Has selectable sub-modes and levels of sub-modes
  G: IR receive mode
  C: IR + Warning mode (put out SOS)
  B: Hypothermia mode
  V: Sound Output mode
    Has selectable sub-modes and levels of sub-modes
  F: Backlights/ Display mode
IR controlled: W, IR, RGB, UV, speaker, backlights
Reed switch master shutoff switch
PTC short-circuit protection switch
Thermometer to measure White LED (including IR control):
  auto LED lower power when >70C and beep warning
  LED shutoff when >90C and beep warning
USB battery charge or external wall mount charge (5V)
Battery Level indicator: L-H: red, yellow, green, blue
Periodically sends out IR signal (mode, device)
Latching main switch
IR, RGB, and IR LED’s embedded in lens
CZ on top of R,G,B controllable LED
Other various magnets and a key ring
WDT enabled to ensure continued running of MCU
Plastic case & glued parts for ruggedness
≤250 Lumens of light output

## Slide 7: 2.1 Parts
Chapter 2 deals with parts needed for the AG:XF flashlight and its companion electronics.
Section 2.2 covers the parts needed for the AG:XF01-2008/WTMCE, divided into 4 sections.
  Electronics
  Casing
  Misc.
  Tools
Pages will be devoted for companion electronics.

## Slide 8: 2.2 AG:XF
Electronics
  (1) PIC16F684 (SMD)
  (1) Li-Ion Cell
  (1) CREE XR-E Q5 LED
  (1) DPDT latching pushbutton switch
  (3) .2” sq switches
  (1) IR LED
  (1) RGB LED
  (1) UV LED
  (1) Small Speaker
  (1) 5mm Reed Switch
  (1) 1.5A PTC resettable fuse
  (7) Female DIP sockets
  (1) IC switch TS5A3166
  (1) Li-Ion charger STC4054
  (2) SOT-23 NPN transistors
  (1) IR sensor TSOP34838
  (1) 10KΩ (25oC) NTC thermistor
  (2) 1uF capacitors [603,603]
  (1) R,G,B LED SMD (1210)
  (3) Red SMD LED [1206,603,603]
  (1) Orange SMD LED [603]
  (2) Yellow SMD LED [1206,603]
  (2) Green SMD LED [1206,603]
  (3) Blue SMD LED [1206,1206,603]
  (2) White SMD LED [603,603]
  (1) 3V Zener Diode
  (3) small (<.7v) Vf Diodes
  (3) 100Ω resistors [603,603,603]
  (1) 220Ω resistor [1206]
  (2) 470Ω resistor [1206,1206]
  (2) 1kΩ resistor [603,603]
  (2) 3.3kΩ resistor [603,603]
  (1) 3.9kΩ resistor [603]
  (1) 4.7kΩ resistor [603]
  (2) 10kΩ resistor [603,603]
  (1) 18kΩ resistor [603]
  (3) 20kΩ resistor [603,603,603]
  (2) 22kΩ resistor [603,603]
  (1) 27kΩ resistor [603]
  (2) 100kΩ resistor [603,603]
  (1) 1MΩ resistor [603]
Casing
  Acrylic tube .5”ID x .625”OD
  Epoxy
  Glue gun glue
  Clear Silicone RTV
Misc.
  Silicone Putty
  2-part clear casting urethane
  Wire-wrap wire (30 gauge)
  Solder
  Indalloy 117
  PCB (see layout)
  (4) magnets 1/8”ID x 3/8”OD x 1/8” thick
  (2) magnets 1/16”ID x ½”OD x 1/16” thick
  ¼” spherical bead
  5mm cubic zircon
  Red, Yellow, Blue, White, Black Acrylic paints
  Warning, XF, owner, contact labels, laminated
  Straw
  Thermal Compound
  Silicone Cap
  Magnetic LED leads
Tools
  Glue gun
  Soldering Iron
  DREMEL tool with circular diamond saw
  Needle-nose pliers
  Wire strippers
  Wire cutters
  Ruler
  Tape
  Holding implements (helping hand)

## Slide 9: 2.3 Pot. Key
Electronics
  (1) 10k Potentiometer [2mm sq]
  (2) White SMD LED [603]
  (1) 10k resistor [603]
Casing
  Epoxy
  Glue gun glue
Misc.
  Solder
  Indalloy 117
  Magnetic LED leads
  Wire wrap wire [30 gauge]
Tools
  Soldering Iron
  Glue gun
  Needle Nose Pliers
  Wire strippers
  Wire cutters
  Tape and holding implements

## Slide 10: 2.4 AG:XF remote
Electronics
Casing
Misc.
Tools

## Slide 11: 3.1 Physical Design
Chapter 3 deals with the original and updated designs along with diagramed pictures.
Section 3.2 deals with original designs.
Section 3.3 deals with current designs.
Section 3.4 deals with a diagrammed photograph.
Section 3.5 deals with the PCB layout.

## Slide 12: 3.2 Original AG:XF Design

## Slide 13: 3.3 Final Design

## Slide 14: 3.4 Diagram
lens
“heat sink”
10k pot acting as “key”
Charging Ports (and Li-Ion Charger)
Li-Ion
IR LED
RGB LED
IR Switch
RGB Switch
Main Switch
IR Sensor
(Q5 LED)
Charge Indicator
Master Magnets
Speaker
Key Ring
(Master Safety Circuitry)
lens
PCB control circuit
10k pot acting as “key”
Charging Ports (and Li-Ion Charger)
Li-Ion
UV LED
RGB LED
UV Switch
RGB Switch
Main Switch
IR Sensor
(Q5 LED)
Charge Indicator
Master Magnets
Speaker
Key Ring
(Master Safety Circuitry)
PIC16F684

## Slide 15: 3.5 PCB layout
O LED (+)
R LED (+)
W/B LED (+)
Cell tester (To In)
Positive sup.
Ground
IR/UV LED (-)
IR Sensor (To Out)
B ILED (-)
G ILED (-)
R ILED (-)
SPK (-)
RGB LED (+)
UV LED (+)
NTC (-)
XR-E Q5 LED (-)
RGB LED (-)
IR LED (+)
MSW (To Out)
1
O LED (+)
R LED (+)
W/B LED (+)
Cell tester (To In)
Positive sup.
Ground
IR/UV LED (-)
IR Sensor (To Out)
B ILED (-)
G ILED (-)
R ILED (-)
SPK (-)
RGB LED (+)
UV LED (+)
NTC (-)
XR-E Q5 LED (-)
RGB LED (-)
IR LED (+)
MSW (To Out)
1
O LED (+)
R LED (+)
W/B LED (+)
Cell tester (To In)
Positive sup.
Ground
IR/UV LED (-)
IR Sensor (To Out)
B ILED (-)
G ILED (-)
R ILED (-)
SPK (-)
RGB LED (+)
UV LED (+)
NTC (-)
XR-E Q5 LED (-)
RGB LED (-)
IR LED (+)
MSW (To Out)
1
O LED (+)
R LED (+)
W/B LED (+)
Cell tester (To In)
Positive sup.
Ground
IR/UV LED (-)
IR Sensor (To Out)
B ILED (-)
G ILED (-)
R ILED (-)
SPK (-)
RGB LED (+)
UV LED (+)
NTC (-)
XR-E Q5 LED (-)
RGB LED (-)
IR LED (+)
MSW (To Out)
1

## Slide 16: 4.1 Schematic Diagram
Chapter 4 deals with specifications of the circuit.
Section 4.2 will deal with the designations for each of the I/O ports of the PIC16F684 chip.
Section 4.3 will deal with the entire circuit’s schematic diagram.

## Slide 17: 4.2 Port Designations
PIC 16F684
RA1
RA0
RA2
RA4
RA3
RA5
RC1
RC0
RC2
RC4
RC5
RC3
IR I
SW I
SPK O
BKLT O
WL O
TEMP I
IRL O
RGBL O
UVL O
RL O
GL O
BL O
AN0
AN1
AN2
AN3
AN4
AN5
AN6
AN7
PWMA

## Slide 18
PA1
PA0
+
Li-Ion
3.7V
PTC
1.5A
S4
Reed
C2
1uF
D6
B
R12
20k
R11
20k
S5
D5
XR-E WT
Q1
NPN
R10
100
R9
18k
R8
20k
R7
22k
B
D4
R
G
R6
10k
NTC
R5
S3
S2
S1
D3
UV
D2
RGB
D1
IR
MCU
PIC16F684
R4
100
R3
100k
R2
100k
R1
100
PA2
Vcc
RA5
RA4
RA3
RA0
RA1
RA2
RC0
RC1
RC2
RC5
RC4
RC3
Gnd
+
_
O
R13
27k
D7
R
D1
G
R15
1k
PB2
PB0
PB1
R14
3k3
Li-Ion Charger
U1
STC4054
CHRG
Gnd
Bat
Ic
Vcc
R16
22k
D8
Y
D21
B
R20
470
D15
D16
D17
R21
220
D20
G
D19
Y
D18
R
R19
470
R18
2k2
D14
3V
D13
D12
R
D11
B
D10
W
W
D9
O
U2
TS5A3166
NO
COM
GND
V+
IN
D2
W
D1
W
R2
10k
10k
R1
KEY
R22
10M
AG:XF01-2008/WTMCE
IC Switch
U3
IR Receiver
TSOP34838
R23
1k
10k-RT
Albert Gural
Q2
NPN
SPK
R25
3k3
R24
3k9
R17
4k7
R12
10k
C1
1uF
PC0

## Slide 19: 5.1 Software Flowchart
Due to the complexity of the software flowchart, there will be several pages devoted to the flowchart, along with labels and wireless connectors to avoid confusion between different pages.
Notes:
-IR IN is normally 1, but becomes 0 when it receives an IR signal
-The controllable RGB LED is turned on by outputting a 0
-The ports designated to IR, RGB, and UV LED’s are normally inputs, unless a computer controlled output is neede.
-Initialization should set WDT to ~.1s; I/O ports (see 4.2)
-A set bit command, such as “set Wbit”, will set or clear every bit of the register, so that only one bit may be set at any time.
SW is the main switch
IRS is the IR switch
UVS is the UV switch
RGBS is the RGB switch
Unless otherwise noted, the sides of a decision diamond is a logic “1” and the bottom is a logic “0”.
A “call” command calls a subroutine, then returns
Ports RA<0:2> only become outputs when a test reveals that they are not manually on. This is to prevent a short-circuit; thus preventing a software restart.
For more detail on specific functions, see Chapter 6, assembly code.

## Slide 20
Initialization
Main:
Set W/Wbit on
5.21 Flowchart
Goto M
Set Y/Ybit on
Goto M
W
Y
Set V/Vbit on
Goto M
V
Test Temp;
>45 C
Goto R
Goto B
T
Test Temp;
<0 C
Return
Clear XF STATUS
registers

## Slide 21
5.22 Flowchart
Set C/Cbit on
C
Test SW
Test IRS
Test UVS
Clear ports
CLRWDT; IROut
based on mode
Test RGBS
Goto V
Test RGBS
Goto Y
Call T
CLRWDT; IROut SOS
SOS routine*
pause
*SOS (3Hz for 1s, 1s, 1Hz for 3s, 1s, 3Hz for 1s, 3s, repeat) use this pulse pattern for W LED and 440Hz, 1s on, 1s off for SPK.
Test RGBS
Goto W

## Slide 22
5.23 Flowchart
Test SW
Test IRS
Test UVS
CLRWDT; IROut
based on mode
Test RGBS
Goto V
Test RGBS
Goto Y
Call T
Set Fbit; Clear ports
F
Test RGBS
Goto W
Set backlights
Start timer
Set RGB according to timer
Test time;
>1 min?
Goto W
Clear timer

## Slide 23: 5.24 Flowchart
Set R/Rbit on
R
Clear ports
Test Temp;
>55 C
Goto
Main
Test Temp;
<40 C
Clear ports
Warning beep/
CLRWDT
Test SW
Test Temp;
<45 C
Turn on W LED
25% of key
Set B/Bbit on
B
Clear ports
Test Temp;
<-14 C
Goto
Main
Test Temp;
>5 C
Test SW
Turn on W
LED based
on key
CLRWDT
Test Temp;
>0 C
Flash LED 50%
duty @ 2Hz
CLRWDT; IROut
based on mode
CLRWDT; IROut
based on mode
Warning beep

## Slide 24
5.25 Flowchart
Set G/Gbit on
G
CLRWDT; IROut
based on mode
Call T
Test IRIn;
Valid?
Y
N
Test IRIn
Clear W LED
& Speaker*
Set W LED &
Speaker
Call T
Test IRIn;
Device?
Y
N
Put IRCODEI
to register
Clear Ports
Follow code;
Run 49ms
Test IRIn*
Y
N
CLRWDT
*Reading the signal stops when the WDT resets the microcontroller.
Invalid

## Slide 25
Test SW
Test IRS
Test UVS
5.31 Flowchart
M
Clear ports
CLRWDT; IROut
based on mode
Test W bit
Goto
WS
Test Y bit
Goto
YS
Test V bit
Goto
VS
Goto W
Call T
Test RGBS
Goto V
Test RGBS
Goto Y
Test Y bit
Goto C
Test RGBS
Goto F
Test W bit
Goto W

## Slide 26
5.41 Flowchart
WS
Clear ports
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Turn on W LED to SW
val. duty cycle @ 1KHz
CLRWDT

## Slide 27
5.42 Flowchart
YS
Clear ports
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Turn on W LED to SW
val. duty cycle @ 1KHz
CLRWDT
RGBS press
> 1s?
Test bit0 YSMS
Goto
YSMS0
Test bit5 YSMS
Goto
YSMS5
Set YSMS0 bit
Goto
YSMS1
YSMS0
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Flash on W LED ~.01s at
SW val. freq. (.1Hz – 100Hz)
CLRWDT
RGBS press
> 1s?
Set YSMS1 bit
Goto
YSMS2
YSMS1
W LED on .2s
W LED on .2s

## Slide 28
5.42 Flowchart
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Flash on W LED & SPK ~.01s
at SW val. freq. (1Hz – 1KHz)
CLRWDT
RGBS press
> 1s?
Set YSMS2 bit
Goto
YSMS3
YSMS2
W LED on .2s

## Slide 29
5.42 Flowchart
Set YSMS3 bit
YSMS3
Clear ports
Test SW
Call T
Goto M
Y
N
Flash W LED
.1% duty @ 4KHz
CLRWDT
RGBS press
> 1s?
Set YSMS30 bit
Goto
YSMS4
YSMS3
Reg. != 0?
YSMS30
Set YSMS31 bit
YSMS31
Set YSMS33 bit
YSMS33
Set YSMS32 bit
YSMS32
Set YSMS34 bit
YSMS34
Test YSMS30
Y
N
Test YSMS31
Y
N
Test YSMS32
Y
N
Test YSMS33
Y
N
Test YSMS34
Y
N
Flash W LED
2% duty @ 4KHz
Flash W LED
19% duty @ 4KHz
Flash W LED
50% duty @ 4KHz
W LED on
RGBS press
<1s ?
Rotate YSMS3
bits left
bit 5 set?
Goto
YSMS30
W LED on .2s

## Slide 30
5.42 Flowchart
Set YSMS4 bit
YSMS4
Clear ports
Test SW
Call T
Goto M
Y
N
Flash W LED
50% duty @ 10Hz
CLRWDT
RGBS press
> 1s?
Set YSMS40 bit
Goto
YSMS5
YSMS4
Reg. != 0?
YSMS40
Set YSMS41 bit
YSMS41
Set YSMS43 bit
YSMS43
Set YSMS42 bit
YSMS42
Set YSMS44 bit
YSMS44
Test YSMS40
Y
N
Test YSMS41
Y
N
Test YSMS42
Y
N
Test YSMS43
Y
N
Test YSMS43
Y
N
Flash W LED
50% duty @ 5Hz
Flash W LED
50% duty @ 2Hz
Flash W LED
50% duty @ 1Hz
Flash W LED
50% duty @ .1Hz
RGBS press
<1s ?
Rotate YSMS4
bits left
bit 5 set?
Goto
YSMS40
W LED on .2s

## Slide 31
5.42 Flowchart
Set YSMS5 bit
YSMS5
Clear ports
Test SW
Call T
Goto M
Y
N
W LED 2.5Hz,
10s pd, 50% duty
CLRWDT
RGBS press
> 1s?
Set YSMS50 bit
Goto
YSMS0
YSMS5
Reg. != 0?
YSMS50
Set YSMS51 bit
YSMS51
Set YSMS53 bit
YSMS53
Set YSMS52 bit
YSMS52
Set YSMS54 bit
YSMS54
Test YSMS50
Y
N
Test YSMS51
Y
N
Test YSMS52
Y
N
Test YSMS53
Y
N
Test YSMS53
Y
N
W LED 5Hz,
5s pd, 50% duty
W LED 5Hz,
2s pd, 50% duty
W LED 10Hz,
2s pd, 50% duty
W LED 10Hz,
1 s, 50% duty
RGBS press
<1s ?
Rotate YSMS5
bits left
bit 5 set?
Goto
YSMS50
W LED on .2s

## Slide 32
5.43 Flowchart
VS
Clear ports
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Turn on SPK based on SW
val. from .01 – 10Hz
CLRWDT
RGBS press
> 1s?
Test bit0 VSMS
Goto
VSMS0
Test bit5 VSMS
Goto
VSMS5
Set VSMS0 bit
Goto
VSMS1
VSMS0
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Turn on SPK based on SW
val. from 10Hz – 1KHz
CLRWDT
RGBS press
> 1s?
Set VSMS1 bit
Goto
VSMS2
VSMS1
W LED on .2s
W LED on .2s

## Slide 33
5.43 Flowchart
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Turn on SPK based on SW
val. from 1KHz – 64KHz
CLRWDT
RGBS press
> 1s?
Set VSMS2 bit
Goto
VSMS3
VSMS2
W LED on .2s
Test SW
Call T
Goto M
Y
N
Send SW analog
value to reg.
Turn on SPK note based on
SW val. (see table 10.222)
CLRWDT
RGBS press
> 1s?
Set VSMS3 bit
Goto
VSMS4
VSMS3
W LED on .2s

## Slide 34
5.42 Flowchart
Set VSMS4 bit
VSMS4
Clear ports
Test SW
Call T
Goto M
Y
N
SPK 2s of 440Hz
every 2min.
CLRWDT
RGBS press
> 1s?
Set VSMS40 bit
Goto
VSMS5
VSMS4
Reg. != 0?
VSMS40
Set VSMS41 bit
VSMS41
Set VSMS43 bit
VSMS43
Set VSMS42 bit
VSMS42
Set VSMS44 bit
VSMS44
Test VSMS40
Y
N
Test VSMS41
Y
N
Test VSMS42
Y
N
Test VSMS43
Y
N
Test VSMS43
Y
N
SPK 2s of 3.5KHz
every 2min.
SPK 2s of 12KHz
every 2min.
SPK 5s of 3.5KHz
every 10min.
SPK 5s of 12KHz
every 10min.
RGBS press
<1s ?
Rotate VSMS4
bits left
bit 5 set?
Goto
VSMS40
W LED on .2s

## Slide 35
5.43 Flowchart
Set VSMS5 bit
VSMS5
Clear ports
Test SW
Call T
Goto M
Y
N
Play Binary
Song (C Major)
CLRWDT
RGBS press
> 1s?
Set VSMS50 bit
Goto
VSMS0
VSMS5
Reg. != 0?
VSMS50
Set VSMS51 bit
VSMS51
Test VSMS50
Y
N
Test VSMS51
Y
N
Play Birthday
Song (F Major)
RGBS press
<1s ?
Rotate VSMS5
bits left
bit 2 set?
Goto
VSMS50
W LED on .2s

## Slide 36: 6.0 AG:XF01 Assembly Code
For the assembly code for the AG:XF01-2008/WTMCE flashlight, see AG:XF01 OS v1.00

## Slide 37: 7.1 IR Transceiving
Chapter 7 deals with the timing and code characteristics in relation to IR transmitting and receiving of the AG:XF01-2008/WTMCE.

## Slide 38: 7.21 IR Code Timing
The transmission starts with a 2.6ms lead signal followed by 16 data bits separated by 520us silence periods. A data ‘0’ is 520us, while a data ‘1’ is 1040us. The first 6 bits consist the device code, the remaining 10 bits are the instruction code bits. This is repeated every 100ms.

## Slide 39: 7.22 IR Code Timing
Lead Signal
Device Code
Instruction Code
(000001) (1111101000)
13us
38.15 KHz

## Slide 40: 7.3 IR Instruction Code Table*
IR Instruction Codes (AG:XF01 OS v1.00) |  |  |  |  | 
Group | HEX | Instruction | Group | HEX | Instruction
Flashlight Output Codes | 000 | White mode | Instruction Codes | 020-027 | Send Device Code
 | 001 | Red mode |  | 028-02F | IR LED
 | 002 | >55*C (Warning) |  | 030-037 | RGB LED
 | 003 | Blue mode |  | 038-03F | UV LED
 | 004 | <-14*C (Warning) |  | 040-04F | Chromatic Scale
 | 005 | Cyan mode |  | 050-057 | SOS Output
 | 006 | SOS (Warning) |  | 058-05F | Backlight
 | 007 | Yellow mode |  | 060-067 | Binary Song
 | 008 | Violet mode |  | 068-06F | Birthday Song
 | 009 | Flashing mode |  | 070-07F | White LED PWM [(low) = .1% step]
 | 00A | Device Code Out |  | 080-0FF | White LED PWM [(low) = .5% step]
 |  | Unimplemented |  | 100-3FF | Unimplemented
FOC Alt.
00B-01F
IC Alt.
*Also found in section 10.3

## Slide 41: 10.1
Chapter 10 deals with a simplified way to see the various modes and functions split into:
  10.2: XF modes
  10.31: Yellow modes
  10.32: Violet modes
  10.4: IR instructions

## Slide 42: 10.2 Tables
Status LED/ IRCODE: | Mode: | Description: | How to change to mode:
White/ W/ h'0100' | Main output mode | W LED out varies with key setting | Under Y, C, B, V, F mode; hold main switch, then press RGB
Red/ R/ h'0101', h'0102 | Hyperthermia mode | W LED power is cut by 3/4 duty cycle | Under any mode; temp > 45C
Yellow/ Y/ h'0107' | Flashing output mode | W LED flashes according to user | Under W, C, V, F mode; hold IR, then press RGB
Green/ G/ n/a | IR receive mode | Receive IR signals and follow instructions | Under W, Y, G, C, B, V, F mode while no externalities in operation; detects IR signal
Cyan/ C/ h'0105’-h’0106’ | IR + Warning mode | Output an IR SOS signal along with a LED + SPK SOS output | Under Y mode; hold IR, then press RGB
Blue/ B/ h'0103', h'0104 | Hypothermia mode | Same as W mode | Under any mode; temp < 5C
Violet/ V/ h'0108' | Sound output mode | Output a certain sound according to key setting | Under W, Y, C, V, F mode; hold UV, then press RGB
Flashing/ F/ h'0109' | Backlights/ display mode | Display backlights and power level | Under W mode; hold RGB, then press main switch
The first table illustrates the main flashlight modes controlling how the flashlight acts when certain buttons are pressed. The table includes what color the status LED should be, the IROut codes, the mode name, the description of that mode, and how to get to that mode. Note that the flashlight may be in any one of those modes, depending on the surroundings or keypresses. For example, to get to Y mode (Flashing output mode), press and hold the switch to turn on the IR light, then quickly press the switch for RGB. This can only be done in W, C, V, or F mode. Also note that at startup, or after R, G, or B modes are finished, the flashlight will go to W mode. B mode serves as a warning of low temperature, but will not hinder any component from working, since this may help stabilize temperature.
Table 10.11

## Slide 43: 10.31 Tables, cont.
This next table shows the sub-modes and levels of sub-modes for Y. It also includes C mode (SOS). To toggle between sub-modes (rows), hold RGBS at least 1s. To get to SOS mode, hold IR then press RGB, when in Y mode. Within the sub-modes, Levels can be changed according to sub-mode. For example, to change brightness level in “Key control brightness” sub-mode, simply change the port key. To change frequency in “Leveled frequency”, quickly press the RGB switch. Note: in all of these cases, the main switch must be on to switch sub-mode (or levels of the sub modes).
Yellow Mode |  |  |  |  |  |  | 
Mode | Levels |  |  |  |  | Change sub-mode | Change level
Key control brightness (YSMS0) | 0% - 100% duty cycle |  |  |  |  | Hold RGBS > 1s | Change key
Key control frequency (YSMS1) | .1Hz - 100Hz |  |  |  |  | Hold RGBS > 1s | Change key
Key control frequency + sound (YSMS2) | .1Hz – 100Hz |  |  |  |  | Hold RGBS > 1s | Change key
Leveled brightness (YSMS3) | 0.1% duty | 1.95% duty | 18.75% duty | 50% duty | 100% duty | Hold RGBS > 1s | Tap RGBS
Leveled frequency (YSMS4) | 10Hz | 5Hz | 2Hz | 1Hz | .1Hz | Hold RGBS > 1s | Tap RGBS
Leveled pulse frequency out (YSMS5) | 5Hz, .1Hz @ 50% | 5Hz, .2Hz @ 50% | 10Hz, .2Hz @ 50% | 10Hz, 1Hz @ 50% | 20Hz, 2Hz @ 50% | Hold RGBS > 1s | Tap RGBS
Alarm signal (C Mode) | SOS (3Hz for 1s, 1s, 1Hz for 3s, 1s, 3Hz for 1s, 3s, repeat) and alarm sound |  |  |  |  | Hold IR, press RGB | n/a
Table 10.21
Bit 0
Bit 1
Bit 2
Bit 3
Bit 4

## Slide 44: 10.32 Tables, cont.
This next table shows the sub-modes and levels of sub-modes for V. To toggle between sub-modes (rows), hold RGB switch for at least a second. Within the sub-modes, levels can be changed according to sub-mode. For example, to change frequency level in “Low-Frequency” sub-mode, simply change the port key. To change the beep pattern in “Periodic Beep”, tap the RGB switch. Note: in all of these cases, the main switch must be on to switch sub-mode (or levels of the sub modes). Also, the frequency and cycle width of the chromatic scale levels are provided in table 10.222. For example, to get a ‘D’ at 4MHz osc., turn SPK on for 851 instruction cycles, then off 852 instruction cycles and repeat or turn SPK on for 1 cycle and off for 1702-03 cycles.
Violet Mode |  |  |  |  |  |  | 
Sub-Mode | Levels |  |  |  |  | Change sub-mode | Change level
LF (VSMS0) | .01Hz - 10Hz |  |  |  |  | hold RGBS > 1s | Change Key
MF (VSMS1) | 10Hz - 10KHz |  |  |  |  | Hold RGBS > 1s | Change Key
HF (VSMS2) | 1KHz – 100KHz |  |  |  |  | Hold RGBS > 1s | Change Key
Scale (VSMS3) | Mid C - High C (523.2862 - 1046.0251)* |  |  |  |  | Hold RGBS > 1s | Change Key
Periodic Beep (VSMS4) | 2s 440Hz every 2min | 2s 7KHz every 2min | 2s 15KHz every 2min | 5s 7KHz every 10min | 5s 15KHz every 10min | Hold RGBS > 1s | Tap RGBS
Binary/ Birthday (VSMS5) | 0000,0001,…1111,0000, etc. |  |  |  |  | Hold RGBS > 1s | Tap RGBS
Table 10.221
Note
Frequency
# of Cycles
Note
Frequency
# of Cycles
C
261.6431
3822
G
392.0031
2551
C#
277.1619
3608
G#
415.2824
2408
D
293.6858
3405
A
439.9472
2273
D#
311.1388
3214
A#
466.2005
2145
E
329.5979
3034
B
493.8272
2025
F
349.2840
2863
C
523.2862
1911
F#
369.9593
2703
*Table 10.222
Birthday Song

## Slide 45: 10.4 IR Instruction Code Table
IR Instruction Codes (AG:XF01 OS v1.00) |  |  |  |  | 
Group | HEX | Instruction | Group | HEX | Instruction
Flashlight Output Codes | 000 | White mode | Instruction Codes | 020-027 | Send Device Code
 | 001 | Red mode |  | 028-02F | IR LED
 | 002 | >55*C (Warning) |  | 030-037 | RGB LED
 | 003 | Blue mode |  | 038-03F | UV LED
 | 004 | <-14*C (Warning) |  | 040-04F | Chromatic Scale
 | 005 | Cyan mode |  | 050-057 | SOS Output
 | 006 | SOS (Warning) |  | 058-05F | Backlight
 | 007 | Yellow mode |  | 060-067 | Binary Song
 | 008 | Violet mode |  | 068-06F | Birthday Song
 | 009 | Flashing mode |  | 070-07F | White LED PWM [(low) = .1% step]
 | 00A | Device Code Out |  | 080-0FF | White LED PWM [(low) = .4% step]
 |  | Unimplemented |  | 100-3FF | Unimplemented
FOC Alt.
00B-01F
IC Alt.

## Slide 46: 11.1
Chapter 11 details how to operate the flashlight.
Section 11.2 shows parts and functions along with what they do.
Section 11.3 details how to change between modes and settings.
Section 11.4 details more complex features

## Slide 47: 11.2 labeled parts
0. RGB LED
RGB Switch
Mode Status Indicator
PIC16F684 MCU
Main Switch (lighted)
Acrylic Case
AG LOGO (lighted)
Li-Ion Cell
IR sensor
Keychain Attachment
Back Magnet/ RA5 I/O
Speaker
Contact Information
Charge/ Att. Ports
IC Cell Charger (lighted)
Light Exposure Warning
NdFeB Magnets
Safety Circuitry
Key in RA4 I/O
Main Circuit Board (PCB)
Cell Voltage Indicator
UV Switch
Lens
UV LED
IR LED
CREE XR-E Q5 LED
IR Switch
Model and Owner Information
0.
23.
1.
3.
4.
5.
6.
7.
8.
9.
10.
11.
12.
13.
14.
15.
16.
18.
19.
20.
21.
22.
17.
0.
1.
23.
4.
5.
6.
7.
8.
24.
9.
10.
11.
27.
13.
14.
15.
16.
18.
20.
26.
22.
17.
25.
2.
2.

## Slide 48: 11.2 Explanation of Parts
0. RGB LED: Displays a flashing light pattern of different colors
RGB Switch: Turns on RGB LED and is used to change flashlight mode
Mode Status Indicator: Displays a 1-bit color based on flashlight mode
PIC16F684 MCU: “Computer”: Controls much of flashlight
Main Switch (lighted): Turns on pin RA4 to turn on Q5 LED and is used to change flashlight mode
Acrylic Case: Covers parts in tough, see-through plastic)
AG LOGO (lighted): Shows ID#01
Li-Ion Cell: Provides flashlight power
IR sensor: Senses and sends IR signals to MCU to be processed
Keychain Attachment: Attaches to back magnet
Back Magnet/ RA5 I/O: Can hold different attachments and has connection to MCU ping RA5
Speaker: Emits soft tones for Sound Output modes
Contact Information: Shows contact information of owner
Charge/ Att. Ports: Used to charge Li-Ion or get power for Att.
IC Cell Charger (lighted): Charges Li-Ion and shows charge finish
Light Exposure Warning: Label warning about flashlight light intensity
NdFeB Magnets: Stabilizes flashlight up and turns on master switch
Safety Circuitry: Master reed switch and 1.5A PTC resettable fuse
Key in RA4 I/O: Controls pin RA4 (set for brightness and speed controls)
Main Circuit Board (PCB): MCU and many hardware components
Cell Voltage Indicator: Uses B,G,Y,R LED’s to indicate Cell charge level
UV Switch: Turns on UV LED and is used to change flashlight mode
Lens: Contains IR, RGB, and UV LED’s; focuses Q5 LED light
UV LED: Outputs UV light (~395nM)
IR LED: Outputs IR light (~808nM)
CREE XR-E Q5 LED: Main White LED for high brightness output
IR Switch: Turns on IR LED and is used to change flashlight mode
Model and Owner Information: Shows model, owner, and important construction dates

## Slide 49: 11.31 Software Operation
The flashlight has 8 main modes [W,R,Y,G,C,B,V,F], sub-modes, and levels:
  White mode (W): Puts out a PWM White LED light (dependent on RA4 voltage) [get to W by pressing MS&RGBS from Y,C,V,F]
  Red mode (R): Indicates too high LED temperature [get to R by getting Q5(WLED) too hot]
  Yellow mode (Y): Puts out flashing white LED patterns [get to Y by pressing IRS & RGBS from W,C,V]
    Sub-mode 0: Variable brightness [get to YSM0 by holding RGBS>1s from YSM5]
    Sub-mode 1: Variable strobe [get to YSM1 by holding RGBS>1s from YSM0]
    Sub-mode 2: Variable strobe + sound [get to YSM2 by holding RGBS>1s from YSM1]
    Sub-mode 3: Leveled brightness [get to YSM3 by holding RGBS>1s from YSM2]
      Level 0: 0.1% Duty Cycle [get to YSM3L0 by tapping RGBS from YSM3L4 under YSM3]
      Level 1: 2% Duty Cycle [get to YSM3L1 by tapping RGBS from YSM3L0]
      Level 2: 19% Duty Cycle [get to YSM3L2 by tapping RGBS from YSM3L1]
      Level 3: 50% Duty Cycle [get to YSM3L3 by tapping RGBS from YSM3L2]
      Level 4: 100% [get to YSM3L4 by tapping RGBS from YSM3L3]
    Sub-mode 4: Leveled strobe [get to YSM4 by holding RGBS>1s from YSM3]
      Level 0: 10Hz [get to YSM4L0 by tapping RGBS from YSM4L4 under YSM4]
      Level 1: 5Hz [get to YSM4L1 by tapping RGBS from YSM4L0]
      Level 2: 2Hz [get to YSM4L2 by tapping RGBS from YSM4L1]
      Level 3: 1Hz [get to YSM4L3 by tapping RGBS from YSM4L2]
      Level 4: 0.1Hz [get to YSM4L4 by tapping RGBS from YSM4L3]
    Sub-mode 5: Leveled pulsed strobe [get to YSM5 by holding RGBS>1s from YSM4]
      Level 0:
    [incomplete]